## Slide 1: Cyberinfrastructure for Intelligent Water Supply (CIWS) Data Visualization Challenge
Jeffery S. Horsburgh and the CIWS Team
Utah Water Research Laboratory
Department of Civil and Environmental Engineering
Utah State University

## Slide 2: We all use water
How much?
When?
For what purpose?
It’s a limited resource and we live in a dry state with a rapidly growing population.

## Slide 3: Water Data
Your city or water provider records your water use to send you a bill
Monthly?
Quarterly?
What if we could make measurements with very high temporal resolution to reveal water use behavior?

## Slide 4: The Challenge
Given high temporal resolution water use data:
What useful information can you extract from the full resolution data to provide to:
  Water consumers – who might change their behavior
  Water providers – who might be able to more efficiently manage water
  Researchers – who are interested in both behavior and efficient water management

## Slide 5: Smart Metering
High frequency data enables:
  Identifying and characterizing individual water end uses
  Providing information to utilities to better manage water demand
  Providing feedback to water users
  Estimating water-related energy use

## Slide 6: Making Existing Meters Smarter
+
Hypothesis: Computation and disaggregation of individual water use events at the data collection site can effectively “shrink” the Big Data produced by smart meters, overcoming storage and communication bandwidth limitations and providing more timely, decision-relevant information.

## Slide 7: The Challenge Datasets
High-resolution (1 second) water flow measurements for 4 buildings in USU’s Living Learning Center
  Hot water supply
  Hot water return
  Cold water supply
High-resolution (4 second) water flow measurements for 1 residential household

## Slide 8: USU’s Living Learning Center
3 Meters:
  Hot water supply
  Hot water return
  Cold water supply
Observations every 1-second
Cold Use = Cold Supply
Hot Use = Hot Supply – Hot Return
Total Use = Hot Supply + Cold Supply – Hot Return

## Slide 9: USU’s Living Learning Center

## Slide 10: LLC Data

## Slide 11: Single Family Residential Data
Data for a single home
Indoor + outdoor water use
Observations made at the water meter
Pulse count recorded every 4 seconds

## Slide 12: Single Family Residential Data

## Slide 13: We challenge you…
To develop innovative ways to analyze and visualize the data
As an audience, you may focus on:
  Us as water researchers
  Water providers who want to efficiently manage water
  Water consumers who want to save money

## Slide 14: Challenge Details
Everything you need is in GitHub
Prizes: 1st ($500), 2nd ($300), and 3rd ($200) place in two categories:
Single family residential
Multi-unit residential building
Submission Deadline: Friday March 1 at midnight!
https://github.com/UCHIC/CIWS-VisChallenge

## Slide 15: Examples!